## Slide 1
BioRydberg 2.0
Geometry-Aware Quantum Transport
Syed Marjan Ghazi • Pasqal QoolQit Contest 2026
Research question
Can bounded atom geometry and laser controls improve a neutral-atom spatial pattern match to a three-site coherent transport reference?
Method
Biological matrix exponential
Coupling-informed 2D register
QoolQit compile + LocalEmulator
Two-seed bounded differential evolution
Chart: 
| Baseline | Optimized
Held-out RMSE | 0.26497 | 0.23288
12.1% lower held-out RMSE
Result: RMSE 0.2650 → 0.2329 on odd time samples excluded from tuning
Interpretation: improved normalized site-distribution similarity only. The biological hopping and driven Rydberg Hamiltonians remain physically distinct.
Notes: Sources: results/study_summary.json and results/tables/study_metrics.csv, generated with QoolQit 1.4.0. Official model and SDK documentation: https://docs.pasqal.com/qoolqit/. Contest requirements: https://www.pasqal.com/resources/the-qoolqit-contest-is-live/.

## Slide 2
Experience with QoolQit 1.4.0
Local, credential-free execution on Python 3.12.9
What worked well
Dimensionless model
Register geometry, drive amplitude, detuning, and duration stayed readable before hardware compilation.
Composable execution
Register + Drive + QuantumProgram + AnalogDevice + LocalEmulator formed a clear reproducible path.
Useful observables
Site occupations, stored evaluation times, and the register interaction matrix supported direct validation.
Verification
10 automated tests passed, including a compiled local-emulator run.
Challenges and feedback
Initial-state examples
A localized Rydberg initial state materially changes this use case. More QoolQit examples would make that capability easier to discover.
Sweep ergonomics
Compilation and emulation were fast after import, but batch execution, caching, and progress telemetry would simplify optimization studies.
Result extraction
Using QoolQit’s stored result times avoided exact floating-point lookup failures. A documented array-first extraction pattern would help.
Next step
Test local detuning controls and noise robustness, then compile the same transparent workflow for Pasqal hardware when access is available.
No cloud or QPU execution claimed
Notes: Development observations are from the repository's executed experiments and tests. API reference and execution model: https://docs.pasqal.com/qoolqit/. Official source: https://github.com/pasqal-io/qoolqit.